## Slide 1: Computer Memory

## Slide 2: Introduction
Computer memory exhibits the widest range of type, technology, organization, performance, and cost of any feature of a computer system.
No single technology is optimal in satisfying the memory requirements for a computer system.
Computer system is equipped with a hierarchy of memory subsystems, some internal to the system (directly accessible by the processor) and some external (accessible by the processor via an I/O module).

## Slide 3: Key Characteristics of Computer Memory Systems
Notes: The complex subject of computer memory is made more manageable if we classify
memory systems according to their key characteristics. The most important of these
are listed in Table 4.1.

## Slide 4: Memory Hierarchy
Design constraints on a computer’s memory can be summed up by three questions:
  How much, how fast, how expensive
There is a trade-off among capacity, access time, and cost
  Faster access time, greater cost per bit
  Greater capacity, smaller cost per bit
  Greater capacity, slower access time
The way out of the memory dilemma is not to rely on a single memory component or technology, but to employ a memory hierarchy

## Slide 5: Hierarchy List
As one goes down the hierarchy, following occurs:
Decreasing cost per bit,
Increasing capacity,
Increasing access time,
Decreasing frequency of access of the memory by the processor
Registers
L1 Cache
L2 Cache
Main memory
Hard Drive/ Magnetic Disks
Optical
Magnetic Tape

## Slide 6: Locality of Reference
Programs tend to reuse data and instructions they have used recently (subroutines and iterations).
Memory references tend to cluster - over a short period of time, the processor is primarily working with fixed clusters of memory references.
An implication of locality is that we can predict with reasonable accuracy what instructions and data a program will use in the near future based on its accesses in the recent past.
Spatial locality
  tendency of a processor to involve a number of memory locations that are clustered (addresses are near to one another).
Temporal locality
  tendency of a processor to access memory locations that have been used recently.

## Slide 7: Cache and Main Memory

## Slide 8: Cache Read Operation

## Slide 9: Typical Cache Organization

## Slide 10: Cache/Main Memory Structure

## Slide 11: Elements of Cache Design
Cache Size
Line Size
Number of Caches
Cache Mapping
Replacement Algorithms
Write Policy

## Slide 12: Cache Mapping
Direct Mapping
Associative Mapping
Set associative mapping

## Slide 13: Internal Memory

## Slide 14: Internal Memory
Organization
SRAM DRAM
Types of ROM

## Slide 15: External Memory

## Slide 16: Magnetic Tape
Magnetic tape was the first kind of secondary memory.
Still Used as low cost, slowest speed member of the memory hierarchy.
Medium is flexible polyester tape coated with magnetizable material.
Data on the tape are structured as a number of parallel tracks running lengthwise
Serial recording (serpentine recording)
  Data are laid out as a sequence of bits along each track

## Slide 17: Magnetic Disk
A disk is a circular platter constructed of nonmagnetic material, called the substrate, coated with a magnetizable material
  Traditionally the substrate has been an aluminium or aluminium alloy
  Recently glass substrates have been introduced

## Slide 19: Disk Device Terminology
Platter
Outer
Track
Inner
Track
Sector
Actuator
Head
Arm

## Slide 20
A cylinder is the set of tracks at a given radius of a disk pack. i.e. a cylinder is the set of tracks that can be accessed without moving the disk arm. 
All the information on a cylinder can be accessed without moving the read/write arm.

## Slide 21: Disk Layout Methods
Disk storage capacity is limited by the maximum recording density that can be achieved on the innermost track.
Zones farther from the centre contains more bits(more sectors) than zones closer to the centre.

## Slide 23: Physical Characteristics of Disk Systems
Head Motion
  Fixed head (one per head)
  Movable Head (one per surface)
Disk Portability
  Non-removable
  Removable
Sides
  Single Sided
  Double Sided
Platters
  Single Platter
  Multiple Platter
Head Mechanism
  Contact (floppy)
  Fixed gap

## Slide 24: Disk Performance Parameters
When the disk drive is operating the disk is rotating at constant speed.
To read or write the head must be positioned at the desired track and at the beginning of the desired sector on the track
  Track selection involves moving the head in a movable-head system or electronically selecting one head on a fixed-head system.
  Once the track is selected, the disk controller waits until the appropriate sector rotates to line up with the head.
Seek time
  Rotational delay (rotational latency)
  Transfer time

## Slide 25
  Consider a disk with an advertised average seek time of 4 ms, time taken by the head to move from one track to adjacent track is 0.5 ms, rotation speed of 15,000 rpm, and 512-byte sectors with 500 sectors per track. Suppose that we wish to read a file consisting of 2500 sectors for a total of 1.28 Mbytes. Estimate the total time for the transfer.
  For sequential organization (file occupies all sectors on adjacent tracks)
  For random organization (accesses to the sectors are distributed randomly over the disk)

## Slide 26
A distinction is made between physical records and logical records. A logical record is a collection of related data elements treated as a conceptual unit, independent of how or where the information is stored. A physical record is a contiguous area of storage space that is defined by the characteristics of the storage device and operating system. Assume a disk system in which each physical record contains thirty 120-byte logical records. Calculate how much disk space (in sectors, tracks, and surfaces) will be required to store 300,000 logical records if the disk is fixed-sector with 512 bytes/sector, with 96 sectors/track, 110 tracks per surface, and 8 usable surfaces. Ignore any file header record(s) and track indexes, and assume that records cannot span two sectors.

## Slide 27: Other External Memory Examples
Optical Memory
  CD
  DVD
  High Definition optical disks
Solid State Drives

## Slide 28: Reference
Computer Organization and Architecture: Designing for Performance, William Stallings, 9th Edition, Pearson India, 2013.