## Slide 1
Control Unit

## Slide 2
Micro-operations: atomic operations of a processor.
Need to tie sequences together.
  Instruction cycle code (ICC) designates which part of cycle processor is in.

## Slide 3: Fetch Sequence
t1: MAR <- (PC)
t2: MBR <- M(MAR)
PC <- (PC) + ∆
t3: IR <- (MBR)
(tx = time unit/clock cycle)

## Slide 4: Rules for Grouping
Proper sequence must be followed
  MAR <- (PC) must precede MBR <- M(MAR)
Conflicts must be avoided
  Must not read & write same register at same time
  MBR <- M(MAR) & IR <- (MBR) must not be in same cycle

## Slide 5: Control Unit
The control unit is the portion of the processor that:
issues control signals internal to the processor to move data between registers, to cause the ALU to perform a specified function, and to regulate other internal operations.
issues control signals external to the processor to cause data exchange with memory and I/O modules.

## Slide 6: Functional Requirements
Basis for design and implementation of the control unit.
Characterization of the control unit:
  Define the basic elements of the processor.
    ALU
    Registers
    Internal data paths
    External data paths
    Control Unit
  Describe the micro-operations that the processor performs.
    Transfer data between registers
    Transfer data from register to external
    Transfer data from external to register
    Perform arithmetic or logical ops
  Determine the functions that the control unit must perform to cause the micro-operations to be performed.

## Slide 7: Functions of Control Unit
Sequencing
  Causing the CPU to step through a series of micro-operations
Execution
  Causing the performance of each micro-op
This is done using Control Signals

## Slide 8: Control Unit

## Slide 9: Data Paths and Control Signals

## Slide 10: Hardwired Implementation
In a hardwired implementation, the control unit is essentially a logic circuit, featuring a finite number of gates.
Its input logic signals are transformed into a set of output logic signals, which are the control signals.
Design uses a fixed architecture—it requires changes in the wiring if the instruction set is modified or changed.

## Slide 11
Hardwired Implementation

## Slide 12: Micro-programmed Control
Microprogrammed control is a control mechanism that generates control signals by reading the memory called control memory that contains control words.
Use sequences of instructions to control complex operations.
Called micro-programming.
Firmware: Firmware is a pre written program that is stored in ROM. It configures the computer and not easily modified by users.
Microinstruction: an instruction stored in control memory. It is a set of micro-operations occurring in the same unit of time.

## Slide 13: Organization of Control Memory

## Slide 14: Micro-instruction Types
Horizontal
Vertical

## Slide 15: Microprogrammed Control Unit

## Slide 16: Reference
Computer Organization and Architecture: Designing for Performance, William Stallings, 6th Edition, Pearson India.