## Slide 1: Cache Basics and Operation

## Slide 2: Cache
Generically, any structure that “memoizes” frequently used results to avoid repeating the long-latency operations required to reproduce the results from scratch, e.g. a web cache
Most commonly in the on-die context: an automatically-managed memory hierarchy based on SRAM
  memoize in SRAM the most frequently accessed DRAM memory locations to avoid repeatedly paying for the DRAM access latency

## Slide 3: Caching Basics
Block (line): Unit of storage in the cache
  Memory is logically divided into cache blocks that map to locations in the cache
On a reference:
  HIT: If in cache, use cached data instead of accessing memory
  MISS: If not in cache, bring block into cache
    Maybe have to kick something else out to do it
Some important cache design decisions
  Placement: where and how to place/find a block in cache?
  Replacement: what data to remove to make room in cache?
  Granularity of management: large or small blocks? Subblocks?
  Write policy: what do we do about writes?
  Instructions/data: do we treat them separately?

## Slide 4: Cache Abstraction and Metrics
Address
Tag Store
(is the address
in the cache?
+ bookkeeping)
Data Store
(stores
memory
blocks)
Hit/miss?
Data

## Slide 5: A Basic Hardware Cache Design
We will start with a basic hardware cache design
Then, we will examine a multitude of ideas to make it better

## Slide 6: Blocks and Addressing the Cache
Memory is logically divided into fixed-size blocks
Each block maps to a location in the cache, determined by the index bits in the address
  used to index into the tag and data stores
Cache access:
  1) index into the tag and data stores with index bits in address
  2) check valid bit in tag store
  3) compare tag bits in address with the stored tag in tag store
If a block is in the cache (cache hit), the stored tag should be valid and match the tag of the block
8-bit address
tag
index
byte in block
3 bits
3 bits
2b

## Slide 7: Direct-Mapped Cache: Placement and Access
Assume byte-addressable memory: 256 bytes, 8-byte blocks  32 blocks
Assume cache: 64 bytes, 8 blocks
  Direct-mapped: A block can go to only one location
  Addresses with same index contend for the same location
    Cause conflict misses
Tag store
Data store
Address
tag
index
byte in block
3 bits
3 bits
2b
V
tag
=?
MUX
byte in block
Hit?
Data
Block: 00000
Block: 00001
Block: 00010
Block: 00011
Block: 00100
Block: 00101
Block: 00110
Block: 00111
Block: 01000
Block: 01001
Block: 01010
Block: 01011
Block: 01100
Block: 01101
Block: 01110
Block: 01111
Block: 10000
Block: 10001
Block: 10010
Block: 10011
Block: 10100
Block: 10101
Block: 10110
Block: 10111
Block: 11000
Block: 11001
Block: 11010
Block: 11011
Block: 11100
Block: 11101
Block: 11110
Block: 11111
Main memory

## Slide 8: Direct-Mapped Caches
Direct-mapped cache: Two blocks in memory that map to the same index in the cache cannot be present in the cache at the same time
  One index  one entry
Can lead to 0% hit rate if more than one block accessed in an interleaved manner map to the same index
  Assume addresses A and B have the same index bits but different tag bits
  A, B, A, B, A, B, A, B, …  conflict in the cache index
  All accesses are conflict misses

## Slide 9: Set Associativity
Addresses 0 and 8 always conflict in direct mapped cache
Instead of having one column of 8, have 2 columns of 4 blocks
Tag store
Data store
V
tag
=?
V
tag
=?
Address
tag
index
byte in block
3 bits
2 bits
3b
Logic
MUX
MUX
byte in block
Key idea: Associative memory within the set
+ Accommodates conflicts better (fewer conflict misses)
-- More complex, slower access, larger tag store
SET
Hit?

## Slide 10: Higher Associativity
4-way
+ Likelihood of conflict misses even lower
-- More tag comparators and wider data mux; larger tags
Tag store
Data store
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?

## Slide 11: Full Associativity
Fully associative cache
  A block can be placed in any cache location
Tag store
Data store
=?
=?
=?
=?
=?
=?
=?
=?
MUX
MUX
byte in block
Logic
Hit?

## Slide 12: Associativity (and Tradeoffs)
Degree of associativity: How many blocks can map to the same index (or set)?
Higher associativity
  ++ Higher hit rate
  -- Slower cache access time (hit latency and data access latency)
  -- More expensive hardware (more comparators)
Diminishing returns from higher
  associativity
associativity
hit rate

## Slide 13: Issues in Set-Associative Caches
Think of each block in a set having a “priority”
  Indicating how important it is to keep the block in the cache
Key issue: How do you determine/adjust block priorities?
There are three key decisions in a set:
  Insertion, promotion, eviction (replacement)
Insertion: What happens to priorities on a cache fill?
  Where to insert the incoming block, whether or not to insert the block
Promotion: What happens to priorities on a cache hit?
  Whether and how to change block priority
Eviction/replacement: What happens to priorities on a cache miss?
  Which block to evict and how to adjust priorities

## Slide 14: Eviction/Replacement Policy
Which block in the set to replace on a cache miss?
  Any invalid block first
  If all are valid, consult the replacement policy
    Random
    FIFO
    Least recently used (how to implement?)
    Not most recently used
    Least frequently used?
    Least costly to re-fetch?
      Why would memory accesses have different cost?
    Hybrid replacement policies
    Optimal replacement policy?

## Slide 15: Implementing LRU
Idea: Evict the least recently accessed block
Problem: Need to keep track of access ordering of blocks
Question: 2-way set associative cache:
  What do you need to implement LRU perfectly?
Question: 4-way set associative cache:
  What do you need to implement LRU perfectly?
  How many different orderings possible for the 4 blocks in the set?
  How many bits needed to encode the LRU order of a block?
  What is the logic needed to determine the LRU victim?

## Slide 16: Approximations of LRU
Most modern processors do not implement “true LRU” (also called “perfect LRU”) in highly-associative caches
Why?
  True LRU is complex
  LRU is an approximation to predict locality anyway (i.e., not the best possible cache management policy)
Examples:
  Not MRU (not most recently used)
  Victim-NextVictim Replacement: Only keep track of the victim and the next victim

## Slide 17: Cache Replacement Policy: LRU or Random
LRU vs. Random: Which one is better?
  Example: 4-way cache, cyclic references to A, B, C, D, E
    0% hit rate with LRU policy
Set thrashing: When the “program working set” in a set is larger than set associativity
  Random replacement policy is better when thrashing occurs
In practice:
  Depends on workload
  Average hit rate of LRU and Random are similar
Best of both Worlds: Hybrid of LRU and Random
  How to choose between the two? Set sampling

## Slide 18: What Is the Optimal Replacement Policy?
Belady’s OPT
  Replace the block that is going to be referenced furthest in the future by the program
  Belady, “A study of replacement algorithms for a virtual-storage computer,” IBM Systems Journal, 1966.
  How do we implement this? Simulate?
Is this optimal for minimizing miss rate?
Is this optimal for minimizing execution time?
  No. Cache miss latency/cost varies from block to block!
  Two reasons: Remote vs. local caches and miss overlapping

## Slide 19: What’s In A Tag Store Entry?
Valid bit
Tag
Replacement policy bits
Dirty bit?
  To reduce the frequency of writing back blocks on replacement, a feature called the dirty bit is commonly used.
  This status bit indicates whether the block is dirty (modified while in the cache) or clean (not modified).
  If it is clean, the block is not written back on a miss, since identical information to the cache is found in lower levels.

## Slide 20: Handling Writes (I)
  When do we write the modified data in a cache to the next level?
    Write through: At the time the write happens
    Write back: When the block is evicted
  Write-back
    + Can combine multiple writes to the same block before eviction
      Potentially saves bandwidth between cache levels + saves energy
  -- Need a bit in the tag store indicating the block is “dirty/modified”
  Write-through
    + Simpler
    + All levels are up to date. Consistency: Simpler cache coherence because no need to check close-to-processor caches’ tag stores for presence
    -- More bandwidth intensive; no combining of writes

## Slide 21
Write-through is easier to implement than write-back. The cache is always clean, so unlike write-back read misses never result in writes to the lower level.
Write-through also has the advantage that the next lower level has the most current copy of the data, which simplifies data coherency.

## Slide 22
There are two options on a write miss:
■ Write allocate—The block is allocated on a write miss, followed by the write hit actions above. In this natural option, write misses act like read misses.
■ No-write allocate—This apparently unusual alternative is write misses do not affect the cache. Instead, the block is modified only in the lower-level memory.

## Slide 23: Cache Parameters vs. Miss/Hit Rate
Cache size
Block size
Associativity
Replacement policy
Insertion/Placement policy

## Slide 24: Cache Size
Cache size: total data (not including tag) capacity
  bigger can exploit temporal locality better
  not ALWAYS better
Too large a cache adversely affects hit and miss latency
  smaller is faster => bigger is slower
  access time may degrade critical path
Too small a cache
  doesn’t exploit temporal locality well
  useful data replaced often
Working set: the whole set of data the executing application references
  Within a time interval
hit rate
cache size
“working set”
size

## Slide 25: Block Size
Block size is the data that is associated with an address tag
  not necessarily the unit of transfer between hierarchies
    Sub-blocking: A block divided into multiple pieces (each w/ V/D bits)
Too small blocks
  don’t exploit spatial locality well
  have larger tag overhead
Too large blocks
  too few total # of blocks  less
    temporal locality exploitation
  waste of cache space and bandwidth/energy
  if spatial locality is not high
hit rate
block
size

## Slide 26: Associativity
How many blocks can be present in the same index (i.e., set)?
Larger associativity
  lower miss rate (reduced conflicts)
  higher hit latency and area cost (plus diminishing returns)
Smaller associativity
  lower cost
  lower hit latency
    Especially important for L1 caches
Is power of 2 associativity required?
associativity
hit rate

## Slide 27: Classification of Cache Misses
Compulsory miss
  first reference to an address (block) always results in a miss
  subsequent references should hit unless the cache block is displaced for the reasons below
Capacity miss
  cache is too small to hold everything needed
  defined as the misses that would occur even in a fully-associative cache (with optimal replacement) of the same capacity
Conflict miss
  defined as any miss that is neither a compulsory nor a capacity miss

## Slide 28: How to Reduce Each Miss Type
Compulsory
  Caching cannot help
  Prefetching can: Anticipate which blocks will be needed soon
Conflict
  More associativity
  Other ways to get more associativity without making the cache associative
    Victim cache
    Better, randomized indexing
    Software hints?
Capacity
  Utilize cache space better: keep blocks that will be referenced
  Software management: divide working set and computation such that each “computation phase” fits in cache

## Slide 29: How to Improve Cache Performance
Three fundamental goals
Reducing miss rate
  Caveat: reducing miss rate can reduce performance if more costly-to-refetch blocks are evicted
Reducing miss latency or miss cost
Reducing hit latency or hit cost
The above three together affect performance

## Slide 30: Restructuring Data Access Patterns (I)
Idea: Restructure data layout or data access patterns
Example: If column-major
  x[i+1,j] follows x[i,j] in memory
  x[i,j+1] is far away from x[i,j]
This is called loop interchange
Other optimizations can also increase hit rate
  Loop fusion, array merging, …
What if multiple arrays? Unknown array size at compile time?
Poor code
for i = 1, rows
for j = 1, columns
sum = sum + x[i,j]
  Better code
  for j = 1, columns
  for i = 1, rows
  sum = sum + x[i,j]

## Slide 31: Restructuring Data Access Patterns (II)
Blocking
  Divide loops operating on arrays into computation chunks so that each chunk can hold its data in the cache
  Avoids cache conflicts between different chunks of computation
  Essentially: Divide the working set so that each piece fits in the cache
But, there are still self-conflicts in a block
  1. there can be conflicts among different arrays
  2. array sizes may be unknown at compile/programming time

## Slide 32: Restructuring Data Layout (I)
Pointer based traversal (e.g., of a linked list)
Assume a huge linked list (1B nodes) and unique keys
Why does the code on the left have poor cache hit rate?
  “Other fields” occupy most of the cache line even though rarely accessed!
struct Node {
struct Node* next;
int key;
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access other fields of node
}
node = nodenext;
}

## Slide 33: Restructuring Data Layout (II)
Idea: separate frequently-used fields of a data structure and pack them into a separate data structure
Who should do this?
  Programmer
  Compiler
    Profiling vs. dynamic
  Hardware?
  Who can determine what is frequently used?
struct Node {
struct Node* next;
int key;
struct Node-data* node-data;
}
struct Node-data {
char [256] name;
char [256] school;
}
while (node) {
if (nodekey == input-key) {
// access nodenode-data
}
node = nodenext;
}

## Slide 34: Cache Optimization

## Slide 35: Six basic cache optimizations
Larger block size to reduce miss rate
  The simplest way to reduce the miss rate is to take advantage of spatial locality and increase the block size.
  Larger blocks reduce compulsory misses, but they also increase the miss penalty.
  Because larger blocks lower the number of tags, they can slightly reduce static power.
  Larger block sizes can also increase capacity or conflict misses, especially in smaller caches.
  Choosing the right block size is a complex trade-off that depends on the size of cache and the miss penalty.

## Slide 36: Bigger caches to reduce miss rate
The obvious way to reduce capacity misses is to increase cache capacity.
  Drawbacks include potentially longer hit time of the larger cache memory and higher cost and power.
  Larger caches increase both static and dynamic power.

## Slide 37: Higher associativity to reduce miss rate
Obviously, increasing associativity reduces conflict misses. Greater associativity can come at the cost of increased hit time. As we will see shortly, associativity also increases power consumption.

## Slide 38: Multilevel caches to reduce miss penalty
  A difficult decision is whether to make the cache hit time fast, to keep pace with the high clock rate of processors, or to make the cache large to reduce the gap between the processor accesses and main memory accesses. Adding another level of cache between the original cache and memory simplifies the decision.
  The first-level cache can be small enough to match a fast clock cycle time, yet the second-level (or third-level) cache can be large enough to capture many accesses that would go to main memory.
  The focus on misses in second-level caches leads to larger blocks, bigger capacity, and higher associativity. Multilevel caches are more power efficient than a single aggregate cache. If L1 and L2 refer, respectively, to first- and second-level caches, we can redefine the average memory access time:
Hit timeL1 + Miss rateL1 × (Hit timeL2 + Miss rateL2 × Miss penaltyL2)

## Slide 39: Giving priority to read misses over writes to reduce miss penalty
A write buffer is a good place to implement this optimization. Write buffers create hazards because they hold the updated value of a location needed on a read miss—that is, a read-after-write hazard through memory.
  One solution is to check the contents of the write buffer on a read miss. If there are no conflicts, and if the memory system is available, sending the read before the writes reduces the miss penalty. Most processors give reads priority over writes.
  This choice has little effect on power consumption.

## Slide 40: Avoiding address translation during indexing of the cache to reduce hit time
Caches must cope with the translation of a virtual address from the processor to a physical address to access memory.
A common optimization is to use the page offset—the part that is identical in both virtual and physical addresses—to index the cache

## Slide 41: Ten Advanced Optimizations of Cache Performance
We can classify the ten advanced cache optimizations we examine into five categories based on these metrics:
  Reducing the hit time—Small and simple first-level caches and way prediction. Both techniques also generally decrease power consumption.
  Increasing cache bandwidth—Pipelined caches, multibanked caches, and nonblocking caches. These techniques have varying impacts on power consumption.
  Reducing the miss penalty—Critical word first and merging write buffers. These optimizations have little impact on power.
  Reducing the miss rate—Compiler optimizations. Obviously any improvement at compile time improves power consumption.
  Reducing the miss penalty or miss rate via parallelism—Hardware prefetching and compiler prefetching. These optimizations generally increase power consumption, primarily due to prefetched data that are unused.

## Slide 42: Advanced Cache Optimization
First Optimization: Small and Simple First-Level Caches to Reduce Hit Time and Power
Second Optimization: Way Prediction to Reduce Hit Time
Third Optimization: Pipelined Cache Access to Increase Cache Bandwidth
Fourth Optimization: Nonblocking Caches to Increase Cache Bandwidth
Fifth Optimization: Multibanked Caches to Increase Cache Bandwidth
Sixth Optimization: Critical Word First and Early Restart to Reduce Miss Penalty
Seventh Optimization: Merging Write Buffer to Reduce Miss Penalty
Eighth Optimization: Compiler Optimizations to
Reduce Miss Rate
Ninth Optimization: Hardware Prefetching of Instructions and Data to Reduce Miss Penalty or Miss Rate
Tenth Optimization: Compiler-Controlled Prefetching to Reduce Miss Penalty or Miss Rate